RES 101
Moving a step forward in the quest for Deterministic Networks (DetNet)
V.Addanki, L. Iannone
Telecom-Paris, Paris (France)

---
Motivation
- Traditional analog audio/video standards use single-purpose point-to-point connections
- Digital audio/video standards still use point-to-point interconnects and interfaces
- Excessive cable mass
- Overuse of resources
  - Cost
- Yet, problems:
  - Latency
  - Synchronization
What you see:
James still saying “Hello Paris!”
What you see:
Drummer already started
playing
Screens
Actual Stage
What you hear: “Nothing Else
Matters!”

---
Motivation
- Audio Video Bridging (AVB) [around 2010]
- Switched Ethernet networks
- Primarily for AV
- Requires AVB support on all the devices in the network
  - Scope limited to a fully controlled local area network.
- Goals:
  - Low-latency
  - Reliability
  - Synchronization
Screens
Actual Stage

---
Motivation
- AVB emerged into Time Sensitive Networking (TSN IEEE802.1Q WG) [2012]
- TSN aims at reliable, deterministic, low-latency data transmission over Ethernet networks
- Limited to Link-layer and fully controlled LAN
- Use-cases:
  - Aerospace
  - Automotive
  - Industrial control process
  - Vehicular control
  - Audio/Video streaming
Actual Stage
Image source: https://www.design-reuse.com/articles/46536/an-introduction-to-time-sensitive-networking.html

---
Motivation
- ESPN DC2 for SportsCenter and NFL football, an example of successful TSN deployment
  - 194,000 sq.ft broadcast studio
  - Handles 46Tbps throughput with 60,000 simultaneous signals
  - 7 studios each with layer-2 LANs using TSN standards
    - Each independent studio worked well in forwarding audio reliably with deterministic delays
  - Due to lack of standards-based routing solution, studios were interconnected using dedicated paths
6
Actual Stage

---
Motivation
- “Layer-3 Interconnecting Layer-2 Islands”
- IETF DetNet
- Operates at Layer-3
- Scalability to large networks
- Use-Cases:
  - Professional audio/video
  - Electrical Utilities
  - Building automation systems
  - Wireless and industrial applications
  - Cellular radio
  - Private blockchains for Determinism
Actual Stage

---
Motivation
- Internet standards process [RFC 2026]:
  - Technical excellence
  - Prior implementation and testing
  - Clear, concise, and easily understood documentation
  - Openness and fairness
  - Timeliness
- Implementing, testing & perfecting with LANs is relatively easier than with WANs
  - Additionally, DetNet use-cases involve high degree of safety requirements for equipment and humans
- Simulation tools help in speeding-up the process of development and standardization
  - DeNS: Deterministic Networks Simulator
- Simulation tools help in identifying and debugging the problems of existing mechanism in wide range of scenarios
  - TAPS: Time Aware PIFO Scheduling

---
Outline
- Background
  - TSN standards
  - TSN Queuing and Scheduling
  - TSN state-of-the-art simulator
- DeNS: Deterministic Networks Simulator
- TAPS: Time Aware PIFO Scheduling
- Results
- Conclusion
Actual Stage

---
Background – TSN Standards
IEEE 802.1 TSN Standards
Flow Concept
[flow classification]
Flow Control
[Queuing and Scheduling]
Flow Synchronization
[Time synchronization]
Flow Management
[Stream Reservation]
Flow Integrity
[Frame replication
and elimination]
Screens
Actual Stage

---
Background – TSN Queuing & Scheduling
Time Aware Scheduling (TAS)
[IEEE 802.1Qbv]
Switching Fabric
Gate Control List
T1: 00000001
T2: 11111110
7
5
4
3
1
6
2
0
MisbehavingFlows
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Transmission Selection
Too Late!

---
Background – TSN Queuing & Scheduling
Cyclic Queuing and Forwarding (CQF)
[IEEE 802.1Qch]
Switching Fabric
Gate Control List
T1: 11111111
T2: 11111111
7
5
4
3
1
6
2
0
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Transmission Selection

---
Background – TSN Queuing & Scheduling
- Cyclic Queuing and Forwarding (CQF)
  [IEEE 802.1Qch]
- While CQF brings determinism in queuing delays and in-turn end-to-end latency, it retains the problems of TAS
  - added queuing latency at each hop
  - impact of mis-behaving flows
Cycle-Change
Even Cycle
Odd Cycle
Out

---
Background – TSN state-of-the-art Simulator
Modules do not support full protocol stack implementation
End-hosts only connects to a CBR traffic generator and a sink
- No possibility to add TCP hosts for instance
Switch modules only support standard encap/decap and queuing functionalities
No Layer-3 extensions
No router modules

---
DeNS: Deterministic Networks Simulator

---
DeNS: Deterministic Networks Simulator

---
DeNS: Deterministic Networks Simulator

---
DeNS: Deterministic Networks Simulator

---
TAPS: Time Aware PIFO Scheduling
Switching Fabric
Gate Control List
T1: 00000001
T2: 11111110
Gate-7 Open?
NO
YES
PIFO
1
5
4
3
2
0
6
7
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Transmission Selection

---
Simulation - Topology
DetNet Hosts
DetNet (or) Misbehaving Hosts
TCP (Best-effort) Hosts

---
Simulation - Results
Time Aware Scheduling
+ Traffic Conditioner
Time Aware Scheduling
Time Aware Scheduling
+ Traffic Conditioner
(Drop all out-of-slot arrivals)
Time Aware PIFO Scheduling
+ Traffic Conditioner
Cyclic Queuing and Forwarding
+ Traffic Conditioner
Closer look
Provides bounded low-latency services to all DetNet flows, both scheduled
and sporadic
- Even in the presence of mis-behaving flows

---
Simulation - Results

---
Conclusion
- DeNS simulator provides full protocol stack features, necessary DetNet and TSN modules
  - All the modules of DeNS are compatible with standard modules of INET framework
  - Source code is made available online on GitHub
- TAPS solution provides bounded low-latency service
  - Perhaps it is time to think outside of FIFO queuing for latency critical flows in the context on DetNet

---
Thank you
&
Open for questions